## Slide 1: Implementation of Interface Agility for Duplex Dynamic Spectrum Access Radio Using USRP
Suman Bhunia and Shamik Sengupta
Supported by NSF CAREER grant CNS #1346600

## Slide 2: Outline
Introduction about DSA
Motivation of our work
Some Related Work
Proposed Model
Prototype
Performance Evaluation
Conclusion

## Slide 3: Why Dynamic Spectrum Access?

## Slide 4: Heterogeneous channels in DSA
Dynamic RF environment
  Dynamic spectrum requirement
  Sometimes single spectrum opportunities are not adequate to support users’ requirements
Allocation of spectrum in the form of non-contiguous blocks
Adaptive bandwidth with spectrum demand
Sense for spectrum if PU arrives

## Slide 5: Dynamic heterogeneous virtual interface
splitting spectrum into fixed bandwidth channels or allocating spectrum in per packet basis is not an optimal solution
creating multiple heterogeneous virtual interfaces with a single radio interface
maintaining multiple independent simultaneous communications
transmission and reception simultaneously
dynamically adapting the number of virtual interfaces and parameters of the virtual interfaces when the data rate requirement in a flow changes or PU arrives
throughput of a mesh network can be enhanced up to 48%

## Slide 6: Some related works
Aggregation Aware Spectrum Assignment (AASA) 1
  All users require the same amount of spectrum
  Uses first-fit approach for channel assignments
Maximum Satisfactory Algorithm (MSA) 2
  users may have different spectrum requirements
  Uses best-fit algorithm
Channel Characteristic Aware Spectrum Aggregation algorithm (CCASA) 3
  Considers the heterogeneity of data carrying capacity in spectrum
  Uses sliding window method
D. Chen, Q. Zhang, and W. Jia, “Aggregation aware spectrum assignment in cognitive ad-hoc networks,” in 3rd International Conference on Cognitive Radio Oriented Wireless Networks and Communications, 2008. CrownCom 2008, pp. 1–6, IEEE, 2008.
F. Huang, W. Wang, H. Luo, G. Yu, and Z. Zhang, “Prediction based spectrum aggregation with hardware limitation in cognitive radio networks,” in IEEE 71st Vehicular Technology Conference (VTC 2010-Spring), 2010, pp. 1–5, IEEE, 2010.
J. Lin, L. Shen, N. Bao, B. Su, Z. Deng, and D. Wang, “Channel characteristic aware spectrum aggregation algorithm in cognitive radio networks,” in IEEE 36th Conference on Local Computer Networks (LCN), 2011, pp. 634–639, IEEE, 2011.

## Slide 7: Related Works…
Jello: A MAC Overlay for Dynamic Spectrum Sharing1
  Distributed NC OFDM prototype
  Distributed defragmentation triggered by other SU departure
  Limited sensing window
  Homogenous spectrum
L. Yang, W. Hou, L. Cao, B. Y. Zhao, and H. Zheng, “Supporting demanding wireless applications with frequency-agile radios.,” in Proceedings of the 7th USENIX Conference on Networked Systems Design and Implementation, NSDI 2010, pp. 65–80, 2010.

## Slide 8: Proposed Methodology
System Considerations
  Spectrum Fragmentation
  Per session spectrum allocation
  OFDM and guard bands
  Heterogeneous channels
  Full Duplex
Design challenges
  Interference isolation
  Carrier frequency noise
  Preamble detection
  Frequency offset in SDR

## Slide 9: Prototype
USRP 200/210 SDR transceivers
Connected with laptops for DSP
GNURadio based
Running on Ubuntu 14.04
Channel’s central frequency is initially set to 2.442 GHz
3 types of nodes:
  Transmitter / source
  Receiver / sink
  Transceiver / relay

## Slide 10: Transmitter / source node design

## Slide 11: Receiver / sink design

## Slide 12: Transceiver / relay design

## Slide 13: Signal flow
sd

## Slide 14: Experiment with images
Original image and image with different spectrum availability

## Slide 15: Experiment with multiple flow

## Slide 16: Conclusion
In this paper, we presented a model for dynamic spectrum access in multi-hop networks
Developed with off-the-shelf SDR
Show the usability of adaptive radio interface
Communication with multiple neighbors simultaneously
A gossip-based framework is proposed to negotiate spectrum
The system can achieve up to 48% enhancement for throughput

## Slide 17
Thank You!