## Slide 1: LOS Discovery for Highly Directional Full Duplex RF/FSO Transceivers
S Bhunia, M Khan, S Sengupta and M Yuksel

## Slide 2: Outline
Introduction
Motivation
Proposed Model
Algorithms
Prototype
Performance Evaluation
Conclusion and Future Work

## Slide 3: Directional Transceiver
Concentrate all the radiation energy in one direction
Example:
  Directional Radio Frequency (RF)
  Free Space Optical communication (FSO)
Benefits:
  Higher gain for signal reception
  Avoid unwanted interference
  Security
Problem
  Need Line of Sight (LOS) orientation
  Complex MAC layer protocol
  Mobility ( such as backbot)

## Slide 4: Directional Full Duplex Transceivers
Can transmit and receive simultaneously on same channel
Transmitter and Receiver oriented in same direction
Complex signal processing to cancel transmitter noise in receiver
Data rate increases significantly
Need sophisticated design to discover LOS of a neighbor

## Slide 5: Neighbor Discovery in Directional Transceiver
Discovering LOS between two nodes
  Without any location measurement
  Without any apriori knowledge
Contribution:
  discover each other without any knowledge of neighbor’s location
  chooses angular speed randomly and reinstates after a threshold time
  mechanism works well for both stationary and mobile setting
  can be extended to discover multiple neighbors
  prototype developed using off the shelf hardware

## Slide 6: Outline
Introduction
Motivation
Proposed Model
Algorithms
Prototype
Performance Evaluation
Conclusion and Future Work

## Slide 7: Application
Two PackBots or K-10 Rovers
In-band: No radio or out-of-band channel
GPS-free environment
The PackBot was the first remote controlled robot to enter the Fukushima nuclear facility after the East Japan Earthquake and tsunami in March 2011.

## Slide 8: Strict requirement of LOS

## Slide 9: Outline
Introduction
Motivation
Proposed Model
Algorithms
Prototype
Performance Evaluation
Conclusion and Future Work

## Slide 10: Discovery by continuation rotation
Rotate transceivers
Random angular speed
Both send beacons
Wait for 3-way handshake
Stop rotation upon completion
Restart if not discover for long time
Asynchronous algorithm

## Slide 11: Timing Diagram

## Slide 12: Outline
Introduction
Motivation
Proposed Model
Algorithms
Prototype
Performance Evaluation
Conclusion and Future Work

## Slide 13: Algorithm for neighbor discovery

## Slide 14: State transition diagram

## Slide 15: Outline
Introduction
Motivation
Proposed Model
Algorithms
Prototype
Performance Evaluation
Conclusion and Future Work

## Slide 16: Simulation results
Two static nodes
1112 μs for handshaking
Frame structure similar to WiFi
Data rate of 1Mbps
1,000,000 repetition
Four divergence angles (β)
Determines reset time
Effect of Processing delay

## Slide 17: Simulation results …
Hard boundary of angular speed is not optimal
Boundaries are chosen from simulation
Divergence angle of 3O
The optimal point lie in the blue region

## Slide 19: Choosing optimal α
Simulation for mobile node
Divergence angle of 5o
Varying α
Here optimal α is 0.06

## Slide 20: Outline
Introduction
Motivation
Proposed Model
Algorithms
Prototype
Performance Evaluation
Conclusion and Future Work

## Slide 21: Prototype architecture

## Slide 22: A snapshot of the experiment

## Slide 23: Experiment Results
IR transmitter
divergence angle of 24o
Transmission time 48.44 μs
Processing time 1078.73 μs
Limited angular speed
Speed chosen from (0, ωmax)
Average discovery time 8.53s

## Slide 24: Outline
Introduction
Motivation
Proposed Model
Algorithms
Prototype
Performance Evaluation
Conclusion and Future Work

## Slide 25: Conclusion
Proposed a novel approach for discovering a neighbor
  line-of-sight (LOS) directional links
  in band communication
  rotate the transceivers and send search signals
  method for finding optimal rotational speeds
  reset rotational speed after optimal time
  Reasonable discovery period
  Works both in stationary and mobile scenarios
Future directions:
  in band discovery for 3D
  refinement of LOS

## Slide 26
Thank You!

## Slide 27
Appendix

## Slide 28: Theorems

## Slide 29: Reset angular speed
If neighbors not discovered for long time reset angular speed (ω)
Calculate reset time as:
Optimal reset time
Optimal boundary of angular speed