## Slide 1
LOS Discovery in 3D for Highly Directional Transceivers
Mahmudur Khan∗, Suman Bhunia ‡, Murat Yuksel ∗, and Shamik Sengupta ‡
∗ Electrical and Computer Engineering, University of Central Florida
‡Computer Science and Engineering, University of Nevada, Reno

## Slide 2: Directional Transceivers
Radiates or receives greater power in specific directions
Radio
  High gain antenna
Free-Space-Optical (FSO)
  Transmitter (Laser Diodes, LEDs, VCSELs)
  Receiver (Photodetector)
Lasers…
LEDs…
IrDAs…
VCSELs…

## Slide 3: Advantages
  Avoids unwanted interference
  Low probability of interception and detection.
  Lower probability of jamming
  Ideal for military applications
  Improves spatial reuse
  Higher data transfer rates (10Gbps using FSO)

## Slide 4: Difficulties
Requires Line-of-Sight (LOS)
  Transmitter and Receiver must be aligned
  Any obstruction or poor weather (fog, heavy rain/snow) can increase BER in a bursty manner
Vulnerable against mobility
  LOS alignment must be maintained with mobility or sway!

## Slide 5: Problem Statement and Assumptions
Two UAVs/ Quadcopters
  Observation behind enemy lines
  Monitoring disaster area
Hovering in 3D space
GPS-free environment
Supplementary omni-directional
RF channel
Equipped with
  A mechanically steerable head/arm
  Highly directional transceivers
Half-duplex or full-duplex mode of communication

## Slide 6: LOS Discovery in 3D
Directional transceiver orientation
r = √(x2+y2+z2)
θ = arccos(z/r)
Φ = arctan (y/x)

## Slide 7: LOS Discovery in 3D
Two stages of neighbor discovery
  Initialization
  3D scanning

## Slide 8: LOS Discovery in 3D
Initialization
  Use omni-directional RF
  Determine existence of neighbor
  No GPS, location information not shared
  Agrees on starting time of 3D scanning
  Agrees on angular speed, ω (rad/s or deg/s)

## Slide 9: LOS Discovery in 3D
3D scanning

## Slide 10: LOS Discovery in 3D
Rotational Speed
ω ≤ β/√2τ
τ = ttran + 3*tprop + 2*tproc

## Slide 11: LOS Discovery in 3D
Modified Helix

## Slide 12: LOS Discovery in 3D
Modified Helix

## Slide 13: Simulations and Results
MATLAB
Nodes at random positions
Divergence angle, β (3o, 5o, 7.5o, 12o)
Angular speed, ω (30rpm – 1200rpm)
50,000 runs for each (β, ω) pair

## Slide 14: Simulations and Results
Neighbor discovery time reduces with increase in θ
Larger divegence angle
Smaller discovery time

## Slide 15: Simulations and Results
Neighbor discovery time reduces with increase in ω
Larger divegence angle
Faster rotation
Smaller discovery time

## Slide 16: Simulations and Results
Neighbor discovery time reduces with increase in β and ω (where, ω = β/√2τ)
Larger β and faster ω
Faster LOS discovery

## Slide 17: Future Work
Develop neighbor discovery algorithm for:
  Mobile nodes
  Multiple neighbors
Develop prototype and perform real test-bed experiments.

## Slide 18: Thank You!

## Slide 19: Questions?